| MONITORING FACT SHEET – Hydrographical changes |
| --- |
| Country: | ROMANIA |
| Author: | Otilia Mihail |
| Institute: | Department on Waters, Forests and Fisheries (Ministry of Environment and Climate Change) |

| Title: Hydrographical changes |
| --- |
| 1. General |
| 1.1 Subject area | HYDROGRAPHICAL CHANGES; BLKRO-D7 |

| 1.2 Definition/Description | The approach of MSFD Descriptor 7 is not uniform at EU level; different countries have not the same interpretation of the scope of this descriptor and especially of the definition of “permanent alteration of hydrographical conditions”. Some countries approach this descriptor close related to Environmental Impact Assessment Directive by tracking and recording the licensing applications proposed developments large enough to have the potential to alter hydrographical conditions, other ones, among them Romania, focus their monitoring efforts on hydrologic conditions considering, quite considerable, also the climate variability. Monitoring undertaken for the WFD on hydro-morphological changes in coastal waters is also important for meeting the requirements of the MSFD, especially given that the majority of current permanent alterations to hydrographical conditions arise from human activities occurring in coastal marine waters. The main organizations dealing with the current programme are NIMRD and GeoEcoMar (RWNA is responsible for WFD monitoring related to hydrographic conditions). The program addresses the state and impact parameters related to: water column physical–chemical: temperature, conductivity/salinity, pH, turbidity (in water column and water-sediment interface); physical: currents (velocity, direction), waves (period, height), sea level seabed habitats physical and sedimentology characteristics: bathymetry, grain size, etc. coastal processes: coastal erosion/accretion, etc. Long term data are available for some parameters (temperature, salinity, currents, and sea level), thus trends can be derived. New monitoring tools have been developed so that some parameters (temperature, salinity, turbidity, pH, currents) are measured in near-real time, therefore more valuable information and knowledge are provided for a better understanding of the consequences of changes in hydrological regime on habitats. Sedimentology and physical processes (upwelling, water masses stratification, etc.) will be considered by the programme by developing models/scenarios, marine spatial planning, but this approach is quite poor developed so far. Also the programme addresses the human activities which impacted on the hydrographical conditions by measuring their distribution/extent and intensity. |
| --- | --- |
| 1.3 Competent authority/ies | Ministry of Environment and Climate Change http://www.mmediu.ro/ Department on Waters, Forests and Fisheries - contact point for the Commission |
| 1.4 Monitoring institutions | National Institute for Marine Research and Development “Grigore Antipa”, Constanta http://www.rmri.ro/ - under coordination of the Ministry of National Education National Research and Development Institute for marine Geology and Geoecology, Bucharest http://www.geoecomar.ro/ - under coordination of the Ministry of National Education |
| 1.5 Additional information | Black Sea Commission - BSIMAP http://www.blacksea-commission.org/_bsimap.asp MSFD Guiding Improvements in the Black Sea Integrated Monitoring System (MISIS) project http://www.misisproject.eu Technical and administrative support for joint implementation of MSFD in Bulgaria and Romania http://www.msfdblacksea.eu Integrated Regional monitoring Implementation Strategy in the South European Seas (IRIS -SES) project http://iris-ses.eu/ Towards Integrated Marine Research Strategy and Programmes (SEAS-ERA) project - Strategic Research Agenda for the Black Sea Basin http://www.seas-era.eu/ |
| 2. Monitoring requirements and purpose |
| 2.1 Necessity | Listed below are direct references to the monitoring requirements – EU directives, Black Sea Commission agreements, national plans, research programme requirements, other. |
| MSFD Articles 8 and 11 Annex III | Art.11. 1. On the basis of the initial assessment made pursuant to Article 8(1), Member States shall establish and implement coordinated monitoring programmes for the ongoing assessment the environmental status of their marine waters on the basis of the indicative lists of elements set out in Annex III and the list set out in Annex V, and by reference to the environmental targets established pursuant to Article 10. 2. Member States sharing a marine region or subregion shall draw up monitoring programmes in accordance with paragraph 1 and shall, in the interest of coherence and coordination, endeavour to ensure that: (a) monitoring methods are consistent across the marine region or subregion so as to facilitate comparability of monitoring results; (b) relevant transboundary impacts and transboundary features are taken into account. Art. 8 The results of monitoring program are required for next cycle of assessment of marine waters. To this end, the parameters related to physical-chemical features and habitat types (Annex III, Table 1), as well as impacts (Annex III, Table 2) must be monitored. Annex III, Table 1 Characteristics Physical and chemical features topography and bathymetry of the seabed; annual and seasonal temperature regime and ice cover, current velocity, upwelling, wave exposure, mixing characteristics, turbidity, residence time; spatial and temporal distribution of salinity; pH, pCO2 profiles or equivalent information used to measure marine acidification. Habitat types the predominant seabed and water column habitat type(s) with a description of the characteristic physical and chemical features, such as depth, water temperature regime, currents and other water movements, salinity, structure and substrata composition of the seabed, Annex III, Table 2 Pressures and impacts Interference with hydrological processes significant changes in thermal regime (e.g. by outfalls from power stations), significant changes in salinity regime (e.g. by constructions impeding water movements, water abstraction). |
| WFD Article 8 Annex V | Art. 8 1. Member States shall ensure the establishment of programmes for the monitoring of water status in order to establish a coherent and comprehensive overview of water status within each river basin district 2. These monitoring programmes shall be in accordance with the requirements of Annex V. |
| Habitats | Art. 11 Member States shall undertake surveillance of the conservation status of the natural habitats and species referred to in Article 2 with particular regard to priority natural habitat types and priority species. |
| Environmental Impact Assessment Directive Article 3 | Art. 3 The environmental impact assessment shall identify, describe and assess in an appropriate manner, in the light of each individual case and in accordance with Articles 4 to 12, the direct and indirect effects of a project on the following factors: (a) human beings, fauna and flora; (b) soil, water, air, climate and the landscape |
| Directive 2001/42/EC on the assessment of the effects of certain plans and programmes on the environment (SEA) Article 10 | Art. 10 1. Member States shall monitor the significant environmental effects of the implementation of plans and programmes in order, inter alia, to identify at an early stage unforeseen adverse effects, and to be able to undertake appropriate remedial action. |
| BWD Article 6 Annex III | Art. 6 2. Bathing water profiles shall be reviewed and updated as provided for in Annex III. 3. When establishing, reviewing and updating bathing water profiles, adequate use shall be made of data obtained from monitoring and assessments carried out pursuant to Directive 2000/60/EC that are relevant for this Directive. Annex III 1. The bathing water profile referred to in Article 6 is to consist of: (a) a description of the physical, geographical and hydrological characteristics of the bathing water, and of other surface waters in the catchment area of the bathing water concerned, that could be a source of pollution, which are relevant to the purpose of this Directive and as provided for in Directive 2000/60/EC; |
| Black Sea Commission Convention on the Protection of the Black Sea Against Pollution (Art. 15) and its Protocols | Convention on the Protection of the Black Sea Against Pollution Art. 15. The Contracting Parties shall cooperate in conducting scientific research aimed at protecting and preserving the marine environment of the Black Sea and shall undertake, where appropriate, joint programmes of scientific research, and exchange relevant scientific data and information. Protocol on the Protection of the Marine Environment of the Black Sea from Land-Based Sources and Activities (2009) Art. 11 1. Within the framework of the provisions of, and the monitoring programmes provided for in Art. 15 of the Convention, and if necessary in cooperation with competent international organisations, the Contracting Parties shall: a) Collect information and data on the conditions of the marine environment and coastal areas of the Black Sea as regards its physical, biological and chemical characteristics; c) Systematically asses the state of the marine environment and coastal areas of the Black Sea; 2. The Contracting Parties shall collaborate in establishing a regional monitoring programme as well as compatible national monitoring programmes, and in facilitating data and information storage, retrieval and exchange. |
| Other plans and/or programmes | Natura 2000 http://www.natura2000.ro |
| 2.2 GES criteria | GES criteria and indicators (see Commission Decision of 1 September 2010) relevant for the Romanian programme are indicated in bold: Descriptor 7 7.1. Spatial characterization of permanent alterations Extent of area affected by permanent alterations (7.1.1) 7.2. Impact of permanent hydrographical changes Spatial extent of habitats affected by the permanent alteration (7.2.1) Changes in habitats, in particular the functions provided (e.g. spawning, breeding and feeding areas and migration routes of fish, birds and mammals), due to altered hydrographical conditions (7.2.2). |
| 2.3 Features, pressures and impacts | Features and pressures/impacts (from MSFD Annex III) relevant for the programme are: Characteristics Physical and chemical features topography and bathymetry of the seabed; annual and seasonal temperature regime and ice cover, current velocity, upwelling, wave exposure, mixing characteristics, turbidity, residence time; spatial and temporal distribution of salinity; pH, pCO2 profiles or equivalent information used to measure marine acidification. Habitat types the predominant seabed and water column habitat type(s) with a description of the characteristic physical and chemical features, such as depth, water temperature regime, currents and other water movements, salinity, structure and substrata composition of the seabed. Annex III, Table 2 Pressures and impacts Interference with hydrological processes significant changes in thermal regime (e.g. by outfalls from power stations); significant changes in salinity regime (e.g. by constructions impeding water movements, water abstraction). |
| 2.4 GES | Romania has not given yet GES definition regarding hydrographical conditions, according to MSFD requirements. Although the programme provides quite enough data/information, the poor understanding of the scope of the descriptor has led to lack of a methodology for GES definition (see Section 6). The current programme considerably addresses the natural and climatic variability, so that the difference between the effects resulting from anthropogenic pressures and climatic variability can be determined, but only partially (more knowledge related to the impacts of human activities on hydrographical conditions are needed - see Section 6). |
| 2.5 Environmental targets MSFD Habitats WFD BSC | Romania has not defined yet the environmental targets according to the MSFD requirement. More research is needed for developing the methodology to set up the environmental targets and, further, the programme has to be adapted for collecting the necessary data/information in order to provide qualitatively and/or quantitatively targets definitions (see Section 6). Relevant targets from other obligations (see section 2.1) that are addressed by the monitoring: - maintain the favorable conservation status for relevant habitats and species, in particular those listed in Annexes I and II of the Habitats Directive. - prevent the deterioration of the status of all WB (no deterioration of the status of all WB) SAP (2009) 3.2 Long-term Ecosystem Quality Objectives (EcoQOs) EcoQO 2: Conservation of Black Sea Biodiversity and Habitats. EcoQO 2a: Reduce the risk of extinction of threatened species EcoQO 2b: Conserve coastal and marine habitats and landscapes. To EcoQO 2, BS SAP has awarded a number of management objectives, which overlap many of the MSFD provisions on evaluation, monitoring and determination of good environmental status. However, SAP indicators reflecting specific regional, cross-border issues and priorities, so they do not overlap perfectly over MSFD qualitative descriptors for determining GES. |
| 2.6 Spatial allocation | Table of where monitoring is required EEZ 12-nm zone Coastal waters Transitional waters MSFD X X X - WFD - X X X Habitats X X X X BWD - - X X BSC X X X X |
| 3 Monitoring concept |
| 3.1 General description of relevant subprogrammes in monitoring programme | 1. Seabed habitats physical characteristics Subprogramme ID (4g): BLKRO-D1,6,7_SeabedHabitats_02 Purpose (4k): Environmental state and impacts Elements monitored (9a): Physical and chemical features • topography and bathimetry of seabed; Habitat types • the predominant seabed and water column habitat type(s) with a description of the characteristic physical features, such as depth, structure and substrata composition of the seabed Parameters (9b): physical structure of habitats (sediment characteristics, topography); bathymetry. Agreed common parameters: physical structure of habitats (sediment characteristics, topography); bathymetry. Monitoring method (9c): Side sonar scanning, geological sampling Temporal resolution (9h): yearly 2. Water column – physical characteristics Subprogramme ID (4g): BLKRO-D1,5,7_WaterColumn_01 Purpose (4k): Environmental state and impacts Elements monitored (9a): Physical and chemical features • annual and seasonal temperature regime and ice cover, turbidity • spatial and temporal distribution of salinity Habitat types • the predominant water column habitat type(s) with a description of the characteristic physical and chemical features, such as water temperature regime, salinity; Interference with hydrological processes • significant changes in thermal regime • significant changes in salinity regime Parameters (9b): Temperature, salinity, transparency / turbidity of water column Agreed common parameters: Temperature, salinity, transparency / turbidity of water column Monitoring method (9c): UNESCO, 1988 - CTD temperature, salinity, turbidity; Grasshoff et al, 1998 - salinity (Mohr-Knudsen titration method) Temporal resolution (9h): hourly (mooring buoys-BSS System); daily (at coastal fix stations); 3 monthly (CTD in coastal and territorial waters); 6 monthly (CTD in beyond territorial waters). 3. Water column – hydrological characteristics Subprogramme ID (4g): BLKRO-D1,7_WaterColumn_02 Purpose (4k): Environmental state and impacts Elements monitored (9a): Physical and chemical features • current velocity, upwelling, wave exposure, mixing characteristics, residence time; Habitat types • the predominant water column habitat type(s) with a description of the characteristic physical features, such as currents and other water movement Parameters (9b): sea level; current velocity and direction; wave action (height and period); ice cover (extent) Agreed common parameters: sea level; current velocity and direction; wave action Monitoring method (9c): OTT mechanical sea level recorder, Paroscientific with pressure sensor-digital sea level recorder; ADCP (Accoustic Doppler Current Profiler - Doppler effect); Waves action - NOAA data (Western Black Sea) / visual (coast area); modelled data; ice cover - satellite images, Temporal resolution (9h): hourly (sea level and current -BSS System); 3 daily (wave); 3 monthly (current); special monitoring in case of extreme events (ad-hoc monitoring). 4. Water column – chemical characteristics Subprogramme ID (4g): BLKRO-D1,7_WaterColumn_02 Purpose (4k): Environmental state and impacts Elements monitored (9a): Physical and chemical features • spatial and temporal distribution of nutrients (DIN, TN, DIP, TP, TOC) and oxygen; • pH. Parameters (9b): pH Agreed common parameters: pH Monitoring method (9c): UNESCO, 1988 – CTD pH Temporal resolution (9h): hourly (mooring buoys-BSS System); daily (CTD at coastal fix stations), 3 monthly (CTD in coastal and territorial waters); 6 monthly (CTD in beyond territorial waters) 5. Activities extracting non-living resources (sand, gravel, dredging) Subprogramme ID (4g): BLKRO-Activities_02 Purpose (4k): Human activities causing the pressures Elements monitored (9a): Port operations; Solid waste disposal incl. dredge material; Other marine uses and activities Parameters (9b): Distribution/extent in space and time, intensity Monitoring method (9c): Romanian Waters National Administration, 2009-Planul de management al Dunarii, Deltei Dunarii si cursurile de apa si apele litorale din Dobrogea; ABAD-L 2009 - Master Plan "Protection and Reahabilitation of Coastal Zone" Temporal resolution (9h): as needed 6. Activities with permanent infrastructures (e.g. ports) or structural changes (e.g. coastal defences) Subprogramme ID (4g): BLKRO-Activities_04 Purpose (4k): Human activities causing the pressures Elements monitored (9a): Land claim, coastal defense; Port operations; Submarine cable & pipeline operations Parameters (9b): Distribution/extent in space and time, intensity Monitoring method (9c): Romanian Waters National Administration, 2009 - Planul de management al Dunarii, Deltei Dunarii si cursurile de apa si apele litorale din Dobrogea; ABADL 2009 - Master Plan "Protection and Rehabilitation of Coastal Zone"; Handbook for IMSP Temporal resolution (9h): yearly 7. Activities with permanent infrastructures (oil & gas) Subprogramme ID (4g): BLKRO-Activities_05 Purpose (4k): Human activities causing the pressures Elements monitored (9a): Marine hydrocarbon extraction (oil & gas) Parameters (9b): Distribution/extent in space and time, intensity Monitoring method (9c): questionnaires sent to all offshore operators Temporal resolution (9h): yearly 8. Coastal human activities (recreational sport) Subprogramme ID (4g): BLKRO-Activities_08 Purpose (4k): Human activities causing the pressures Elements monitored (9a): Recreational, incl. yachting Parameters (9b): Distribution/extent in space and time, intensity Monitoring method (9c): questionnaires sent to all agreement harbors and all units providing aquatic sport facilities Temporal resolution (9h): yearly 9. Coastal human activities (tourism, ecotourism) Subprogramme ID (4g): BLKRO-Activities_07 Purpose (4k): Human activities causing the pressures Elements monitored (9a): Tourism Parameters (9b): Distribution/extent in space and time, intensity Monitoring method (9c): Methodological manual for tourism statistic http://epp.eurostat.ec.europa.eu/cache/ITY_OFFPUB/KS-GQ-13-007/EN/KS-GQ-13-007-EN.PDF Temporal resolution (9h): yearly 10. Land-based activities (industry) Subprogramme ID (4g): BLKRO-Activities_09 Purpose (4k): Human activities causing the pressures Elements monitored (9a): Industry (discharges, emissions) Parameters (9b): Distribution/extent in space and time, intensity Monitoring method (9c): questionnaires sent to all operators from the coastal zone Temporal resolution (9h): yearly 11. Land-based activities (agriculture) Subprogramme ID (4g): BLKRO-Activities_10 Purpose (4k): Human activities causing the pressures Elements monitored (9a): Agriculture & forestry (run-off, emissions) Parameters (9b): Distribution/extent in space and time, intensity Monitoring method (9c): questionnaires sent to all farms from the coastal zone and the Danube River catchment area Temporal resolution (9h): yearly 12. Land-based activities (urban) Subprogramme ID (4g): BLKRO-Activities_11 Purpose (4k): Human activities causing the pressures Elements monitored (9a): Urban (municipal waste water discharges) Parameters (9b): Distribution/extent in space and time, intensity Monitoring method (9c): information provided by local authorities and private operators Temporal resolution (9h): yearly 13. Effectiveness of measures to be developed |
| 3.2 Description of monitoring network | NIMRD Monitoring network comprises 45 sampling stations (bottom depths within 5 – 60 m), covering the entire RO coastal waters and, partially, shelf waters. Physical-chemical parameters (temperature, salinity, pH) are measured seasonally at each stations (see Fig. 1) Daily measurements of temperature, salinity, pH, and sea level are carried out at long-term fix coastal station (in the Constanta area). Currents and wave monitoring are performed in the coastal area, by using three Acoustic Doppler Current Profilers Sentinel 600 Hz in fixed underwater measurement locations or during the scientific cruises carried out in the monitoring network (see Fig. 1). Fig. 1 Map of sampling stations of the environment routine monitoring carried out by NIMRD GeoEcoMar Sampling network includes 45 stations with bottom depths between 15 and 200 m, covering the entire RO shelf (Fig. 2). In situ physical-chemical parameters (CTD measurements - pressure/depth, temperature, conductivity/salinity, sigma theta, pH, Eh, light transmission/absorption, turbidity – in water column) and grain-size analyses are performed 2 times/year at each sampling station. Also currents measurements are carried out in the coastal area, but not regularly. Bathymetric measurements covering the entire Romanian shelf waters are performed within the Geological, Sedimentology and Geophysics Mapping Program (scale 1:50000). Fig. 2 Map of Geo-Ecomar sampling network Black Sea Security System (BSSS) – developed (under the Marine Geohazard project) and operated by Geoecomar (RO) and IO-BAS (BG) 3 offshore moored observatories (in RO waters, bottom depths between 72 and 90 m) providing near-real time data (from surface layer and 20 m above seafloor) 1 coastal sampling station (bottom depth of 15m) (Fig. 3) Parameters monitored: pressure, temperature, conductivity/salinity, turbidity, currents. BSSS extends also in the BG waters (2 offshore moored observatories) Fig. 3 Map of offsore moored obsvervatories locations |
| 3.3 Threats, activities and measures | Relevant activities themes/activities related to the programme are: Man-made structures (incl. construction phase)/Port operations; submarine cable and pipeline operations; Placement and operation of offshore structures (other than for energy production); Land/sea physical interaction: land claim, coastal defence Energy production/Marine hydrocarbon (oil and gas) extraction Extraction of non-living resources/ Dredging Food production/Aquaculture Waste disposal/ Solid waste disposal incl. dredge material Land-based activities/industries/Coastal, riverine and athmospheric inputs from land - industrial discharges; Coastal, riverine and atmospheric inputs from land - agricultural run-off, forestry and emissions; Coastal, riverine and atmospheric inputs from land - municipal waste water discharge Recreation/Tourism The programme will address the above mentioned activities by measuring either the distribution in space and time, intensity of some relevant activities or impacts associated (changes in the water column characteristics e.g. temperature, salinity, pH, turbidity, currents; changes in seabed physical characteristics e.g substrata type/structure, bathymetry). The measures which will be monitored by the programme have to be developed. |
| 3.4 Data management | Data are reported (either as processed data or data products) through competent authority to EEA, BSC (through AGs – PMA, LBS, and CBD). Data are also reported in databases belonging to other projects (SeaDataNeet, SESAME, PERSEUS, MISIS) from where they can be accessed in accordance with the terms of such project. Data will be available via national website http://www.rmri.ro and www.nodc.ro (starting with 2015). |
| 4. Assessment |
| 4.1 Assessments | Existing assessments MSFD (Art. 8) – Initial Assessment http://cdr.eionet.europa.eu/ro/eu/msfd8910/msfd4text/envuhwuaq Environmental Status Reports http://www.rmri.ro/Home/Products.EnvStatusReport.html State of Environment Report 2001-2006/7 http://www.blacksea-commission.org/_publ-SOE2009.asp Diagnostic Report for Coastal Zone http://www.rowater.ro/dadobrogea |
| 4.2 Assessment of GES | GES has not been defined yet in terms of D 7 - Hydrographical Conditions. So far, the programme cannot be considered fully adequate (even if it provides quite enough data/information) due to lack of methodology for defining GES and targets (see Section 6). |
| 5. Literature |
|  | Zampoukas, N., Piha, H., 2011, Review of Methodological Standards Related to the Marine Strategy Framework Directive Criteria on Good Environmental Status, Publications Office of the European Union, 53 pp. http://publications.jrc.ec.europa.eu/repository/handle/111111111/16069 Zampoukas, N., Piha, H., Bigagli, E., Hoepffner,N., Hanke, G., Cardoso, A., 2012, Monitoring for the Marine Strategy Framework Directive: Requirements and Options, Publications Office of the European Union, 42 pp., http://publications.jrc.ec.europa.eu/repository/handle/111111111/23169 Zampoukas, N., Piha, H., Bigagli, E., Hoepffner,N., Hanke, G., Cardoso, A., 2013, Marine monitoring in the European Union: how to fulfil the requirements for the MSFD in an efficient and integrated way, Marine Policy, 39, 349-351 http://publications.jrc.ec.europa.eu/repository/handle/111111111/27825 OSPAR Commission, 2012, Advice document on Hydrographical conditions (MSFD Descriptor 7) http://www.ospar.org/documents/dbase/publications/p00583/p00583_advice_document_d7_hydrographic_conditions.pdf |
| 6. Activities required to implement the concept |
| 6.1 Changes to the current monitoring programme | Recommendations and actions needed: increasing financial assistance and securing sustainable financing at national levels; better integration the MSFD monitoring with the monitoring requirements of the other directives (WFD, Habitats, EIA, SEA, etc.) and regional sea conventions (BSC); better use and coordination of the existing capacities of all organizations dealing with the monitoring programme (including monitoring infrastructure sharing) and avoid overlapping of activities and efforts; permanent agreements with other authorities/organizations in supporting the programme (e.g. Maritime Hydrographical Direction, ROSA, local authorities, Port Authorities, etc.); strengthening the regional cooperation/harmonization between the Black Sea MS (common MSFD indicators/parameters to be approach, common methodology for the GES and Environmental Targets definitions, common sampling and data processing methodologies); consultations regarding the potential transboundary effects of the human activities and the measures envisaged to reduce or eliminate such effects; coordinated data and developing methodological standards for monitoring of hydrographical conditions at the scale of marine regions (starting the with identification of existing best practice); adjustment/increasing of temporal and spatial coverage of the program; additional indicators/parameters to be included; more research needed for developing new parameters to be monitored (e.g. pCO2, freshwater input rates, etc); new monitoring tools to be developed (e.g. satellite images, models, marine spatial planning, etc.); improving QA/QC; improving data management. |
| 6.2 Gaps: GES information | The programme will be fully adequate (in terms of providing data and information needed to assess GES) in time for the next assessment in 2018. |
| 6.3 Plans: Plans for GES information | Firstly, a methodology for GES definition has to be developed. However, in order to define GES, the programme has to provide sufficient and valuable information related to the human activities and climate variability. OSPAR, 2012 (see Section 5) recommends to consider only the large-scale human activities, such as coastal defence works, land reclamation projects, structures in coastal or open sea (the small-scale ones are well covered by EIA), which may permanently influence the hydrographical regime of currents, waves and sediments. Further changes in sediment transportation, bed forms, salinity and temperature might lead to subsequently positive or negative impacts on species or/and habitat. All these take place against a background of much broader scale hydrographical changes, induced either by human activities or climatic changes, ocean acidification, etc. More knowledge is needed for developing new tools (models, MSP) to a better understanding of the cumulative effects of the pressures, which should be baseline for the GES definition. The programme should be able to provide adequate data/information for validate the models (financial support and/or better coordination for adjusting spatial and temporal resolution of data acquisition are needed). |
| 6.4 Gaps: Target information | The programme will be fully adequate in terms of collection of data and information needed for assessing the environmental targets in time for the next assessment in 2018. |
| 6.5 Plans: Plans for information on targets | More research is needed for developing the methodology to set up the environmental targets. For this purpose, a major need (according to OSPAR, 2012 – see Section 5) is to develop the models to assess: changes in the condition and extent of areas affected by permanent alterations (this includes changes in currents, upwelling patterns, waves, bathymetry, and salinity). The programme should be able to provide adequate data/information (financial support and/or better coordination for adjusting spatial and temporal resolution of data acquisition are needed) necessary because models should be calibrated and continuously supported and validated with “in situ” monitoring datasets; changes in the spatial extent of habitats affected by permanent alterations, using field data and validated model data; changes in habitats due to altered hydrographical conditions, using field data and validated model data (it is necessary to define the change in function for diverse habitats by interpreting the changes determined in the spatial extent of habitats in terms of food web). Also, close coordination with the Descriptors 1 (Biodiversity), 4 (Food Web) and 6 (Seafloor integrity) will be necessary due to the links between them. Some of the targets defined for these descriptors may also be relevant in relation to Descriptor 7. A link to Descriptor 5 (Eutrophication) should be also made since both are important factors with regard to eutrophication (e.g. in the event that mixing characteristics and/or retention time are changed). |
| 6.5 Plans: Plans for information on measures | To be developed |