| MONITORING FACT SHEET |
| --- |
| Country: | ROMANIA |
| Author: | Vasiliu Dan Lucian |
| Institute: | National Research and Development Institute for Marine Geology and Geoecology - GeoEcoMar |

| MONITORING FACT SHEET TEMPLATE |
| --- |
| Title: Eutrophication |
| 1. General |
| 1.1 Subject area | EUTROPHICATION; BLKRO-D5 |

| 1.2 Definition/Description | Definition of items monitored/description of general approach Eutrophication is a process driven by the nutrient enrichment, especially compounds of nitrogen and/or phosphorus, leading to: increased growth, primary production and algal biomass; changes in the balance of organisms; and water quality degradation. The consequences of eutrophication are undesirable if they appreciably degrade ecosystem health and biodiversity and/or the sustainable provision of goods and services. The eutrophication causes and effects has been sistematically monitored in the Romanian waters (with special emphasis on the coastal waters) for more than 3 decades ago. Over the years, the monitoring programme has been substantially improved (in terms of infrastructure, methodology, etc), now being fairly well developed (coastal and shelf waters). The current monitoring programme is a function of: Size of area to be assessed Number and distribution of land-based sources Existing monitoring strategy (reference areas, former networks, existing long-term data series, existing logistics, etc) Sampling frequency and duration Specificity, sensitivity of analytical technique Magnitude of concentration expected Available resources Its main objective is to characterize present state and trends as well as to identify the environmental impact of human activities as possible causes for observed environmental impairments. The programme’s main objective is to characterize present state and trends as well as to identify the environmental impact of human activities as possible causes for observed environmental impairments. Thus, it addresses to: state and impact parameters: - Physical–chemical: transparency, nutrients (water column and sediment-water interface), TOC, dissolved oxygen/oxygen saturation (water column and sediment-water interface - Biological parameters pelagic community: chlorophyll a, phytoplankton (species composition, abundance – density and biomass) seabed community: phytobenthos (species composition, abundance – biomass) pressures - both at source - nutrient and organic matter loads from point and non-point sources (WWTP, riverine input, agriculture, industrial activities, aquaculture, etc) and in the marine environment (nutrients in the water column) activities (by measuring the extent and intensity) |
| --- | --- |
| 1.3 Competent authority/ies | Ministry of Environment and Climate Change http://www.mmediu.ro/ Department on Waters, Forests and Fisheries - contact point for the Commission |
| 1.4 Monitoring institutions | Romanian Water National Administration (Dobrogea-Litoral Water Basin Administration) http://www.rowater.ro/ - under coordination of the Ministry of Environment and Climate Change National Institute for Marine Research and Development “Grigore Antipa”, Constanta http://www.rmri.ro/ - under coordination of the Ministry of National Education National Research and Development Institute for marine Geology and Geoecology, Bucharest http://www.geoecomar.ro/ - under coordination of the Ministry of National Education |
| 1.5 Additional information | Where can additional information be found (e.g. via a web link) Black Sea Commission - BSIMAP http://www.blacksea-commission.org/_bsimap.asp MSFD Guiding Improvements in the Black Sea Integrated Monitoring System (MISIS) project http://www.misisproject.eu Integrated Regional monitoring Implementation Strategy in the South European Seas (IRIS -SES) project http://www.isotech.com.cy/ Technical and administrative support for joint implementation of MSFD in Bulgaria and Romania No link available yet Towards Integrated Marine Research Strategy and Programmes (SEAS-ERA) project - Strategic Research Agenda for the Black Sea Basin http://www.seas-era.eu/ |
| 2. Monitoring requirements and purpose |
| 2.1 Necessity | Listed below are direct references to the monitoring requirements – EU directives, Black Sea Commission agreements, national plans, research programme requirements, other. |
| MSFD Articles 8, 11 and 13 Annex III | Art.11. 1. On the basis of the initial assessment made pursuant to Article 8(1), Member States shall establish and implement coordinated monitoring programmes for the ongoing assessment the environmental status of their marine waters on the basis of the indicative lists of elements set out in Annex III and the list set out in Annex V, and by reference to the environmental targets established pursuant to Article 10. 2. Member States sharing a marine region or subregion shall draw up monitoring programmes in accordance with paragraph 1 and shall, in the interest of coherence and coordination, endeavour to ensure that: (a) monitoring methods are consistent across the marine region or subregion so as to facilitate comparability of monitoring results; (b) relevant transboundary impacts and transboundary features are taken into account. Art. 8 The results of eutrophication monitoring program are required for next cycle of assessment of marine waters. To this end, the following parameters must be monitored for physical-chemical and biological features (Annex III, Table 1) and pressures/impacts (Annex III, Table 2) to be described: Annex III, Table 1 spatial and temporal distribution of nutrients (DIN, TN, DIP, TP, TOC) and oxygen; description of the biological communities associated with the predominant water column habitats (information on the phytoplankton and zooplankton communities, including the species and seasonal and geographical variability); information on angiosperms, macroalgae, including species composition, biomass and annual/seasonal variability according to seabed habitats. Annex III, Table 2 Inputs of fertilisers and other nitrogen- and phosphorus-rich substances (e.g. from point and diffuse sources, including agriculture, aquaculture, atmospheric deposition), Inputs of organic matter (e.g. sewers, mariculture, riverine inputs). |
| Habitats Article 11 | Art. 11 Member States shall undertake surveillance of the conservation status of the natural habitats and species referred to in Article 2 with particular regard to priority natural habitat types and priority species. |
| WFD Article 8 Annex V | Art. 8 1. Member States shall ensure the establishment of programmes for the monitoring of water status in order to establish a coherent and comprehensive overview of water status within each river basin district. 2. These monitoring programmes shall be in accordance with the requirements of Annex V. |
| NiD Articles 5 and 6 | Art. 5 6. Member States shall draw up and implement suitable monitoring programmes to assess the effectiveness of action programmes established pursuant this Article. Member States which apply Art. 5 throughout their national territory shall monitor the nitrate content of waters at selected measuring points which make it possible to establish the extent of nitrate pollution in the waters from agricultural sources. Art. 6 1. For the purpose of designating and revising the designation of vulnerable zones, Member States shall: c) review the eutrophic state of fresh surface waters, estuarine waters, and coastal waters every four years. |
| UWWTD Article 15 Annexes IB and ID | Art. 15. 1. Competent authorities or appropriate bodies shall monitor: - discharges from urban waste water treatment plants to verify compliance with the requirements of Annex I.B in accordance with the control procedures laid down in Annex I.D, 2. Competent authorities or appropriate bodies shall monitor waters subject to discharges from urban waste water treatment plants and direct discharges as described in Article 13 in cases where it can be expected that the receiving environment will be significantly affected. 3. In the case of a discharge subject to the provisions of Article 6 and in the case of disposal of sludge to surface waters, Member States shall monitor and carry out any other relevant studies to verify that the discharge or disposal does not adversely affect the environment. . |
| BWD Article 6 Article 9 Annex III | Art. 9 Other parameters 1. When the bathing water profile indicates a tendency for proliferation of macro-algae and/or marine phytoplankton, investigations shall be undertaken to determine their acceptability and health risks and adequate management measures shall be taken, including information to the public. |
| Black Sea Commission Convention on the Protection of the Black Sea Against Pollution (Art. 15) and its Protocols | Convention on the Protection of the Black Sea Against Pollution Art. 15. The Contracting Parties shall cooperate in conducting scientific research aimed at protecting and preserving the marine environment of the Black Sea and shall undertake, where appropriate, joint programmes of scientific research, and exchange relevant scientific data and information. The Contracting Parties shall, inter alia, establish through the Commission and, where appropriate, in cooperation with international organizations they consider to be competent, complementary or joint monitoring programmes covering all sources of pollution and shall establish a pollution monitoring system for the Black Sea including, as appropriate, programmes as bilateral or multilateral level for observing, measuring, evaluating and analyzing the risks or effects of pollution of the marine environment of the Black Sea. Protocol on the Protection of the Marine Environment of the Black Sea from Land-Based Sources and Activities (2009) Art. 11 1. Within the framework of the provisions of, and the monitoring programmes provided for in Art. 15 of the Convention, and if necessary in cooperation with competent international organisations, the Contracting Parties shall: a) Collect information and data on the conditions of the marine environment and coastal areas of the Black Sea as regards its physical, biological and chemical characteristics; b) Collect information and data and prepare and maintain an inventory of inputs of substances listed in Annex I of this Protocol, including information on the distribution of sources and quantities of such substances introduced to the marine environment of the Black Sea; c) Systematically asses the state of the marine environment and coastal areas of the Black Sea; d) Systematically assess, as far as possible, the levels of pollution along their coasts, in particular with regard to activities and substances listed in Annex I and periodically to provide information in this respect; 2. The Contracting Parties shall collaborate in establishing a regional monitoring programme as well as compatible national monitoring programmes, and in facilitating data and information storage, retrieval and exchange. |
| Other plans and/or programmes | Comments |
| 2.2 GES criteria | List relevant GES Criteria and characteristics (indicators( (see Commission Decision of 1. September 2010) 5.1. Nutrients levels — Nutrients concentration in the water column (5.1.1) — Nutrient ratios (silica, nitrogen and phosphorus), where appropriate (5.1.2) 5.2. Direct effects of nutrient enrichment — Chlorophyll concentration in the water column (5.2.1) — Water transparency related to increase in suspended algae, where relevant (5.2.2) — Abundance of opportunistic macroalgae (5.2.3) — Species shift in floristic composition such as diatom to flagellate ratio, benthic to pelagic shifts, as well as bloom events of nuisance/toxic algal blooms (e.g. cyanobacteria) caused by human activities (5.2.4) 5.3. Indirect effects of nutrient enrichment — Abundance of perennial seaweeds and seagrasses (e.g. fucoids, eelgrass and Neptune grass) adversely impacted by decrease in water transparency (5.3.1) — Dissolved oxygen, i.e. changes due to increased organic matter decomposition and size of the area concerned (5.3.2). |
| 2.3 Features, pressures and impacts | List relevant features and pressures from MSFD Annex III Refer to section 6 regarding gaps and plans Characteristics Physical and chemical features — spatial and temporal distribution of nutrients (DIN, TN, DIP, TP, TOC) and oxygen, Biological features — a description of the biological communities associated with the predominant seabed and water column habitats (this would include information on the phytoplankton and zooplankton communities, including the species and seasonal and geographical variability), — information on angiosperms and macroalgae, including species composition, biomass and annual/seasonal variability, Pressures and impacts Nutrient and organic matter enrichment — Inputs of fertilisers and other nitrogen — and phosphorus-rich substances (e.g. from point and diffuse sources, including agriculture, aquaculture, atmospheric deposition), — inputs of organic matter (e.g. sewers, mariculture, riverine inputs). |
| 2.4 GES | RO has provided GES definitions at criteria levels: Crt. 5.1. Nutrient concentrations do not lead to an undesirable disturbance to the balance of organisms present in the water or to the quality of the water concerned resulting from accelerated growth of algae, and are within the threshold values as stated in the environmental targets Crt. 5.2. The direct effects of nutrient enrichment associated with algal growth do not constitute or contribute to an undesirable disturbance to the balance of organisms present in the water and to the quality of the water concerned, by meeting the threshold values as stated in the environmental targets Crt. 5.3. Indirect effects of nutrient enrichment associated with growth of macroalgae, seagrass, and reductions of oxygen concentrations do not constitute an undesirable disturbance to the balance of organisms present in the water and to the quality of the water concerned, and are within the threshold values as stated in the environmental targets There should be no kills in benthic animal species as a result of oxygen deficiency that are directly related to anthropogenic input of nutrients. Generaly, the programme provides sufficient data/information for establishing if the descriptor is at GES or not. In the latter case, the data/information could contribute to determine the distance to GES as difference between data provided by the programme and the thresholds set up in the Article 9. Also trends (for some relevant parameters) could be derived from programme and contribute to determine the distance to the GES. However, the programme has to be improved in terms of spatial coverage; the open waters are quite poorly monitored. The programme partially addresses to natural and climatic variability so that, in part, the difference between the effects resulting from anthropogenic pressures and climatic variability could be determined. |
| 2.5 Environmental targets MSFD Habitats WFD NiD UWWTD BSC | Relevant MSFD targets defined in the article 10 reporting RO has defined environmental targets as follows: Indicator 5.1.1 State target: The 75th percentile of annual mean concentrations of nutrients in marine waters not less than target values (set out in the Romanian revised GES report under Arts. 9 and 10 of the MSFD) Pressure targets: DIP and DIN from anthropic input should be constant or decreasing, based on monitoring routine Indicator 5.1.2 Nutrients level maintaining the N/P ratio higher than 10 Indicator 5.2.1 The 75th percentile of summer chlorophyll a concentration in marine waters not less than threshold values (threshold value: 90th percentile of summer chlorophyll a concentrations) Indicator 5.2.2 The 95th percentile of transparency values should be more than the threshold values as set out in the revised GES report Indicator 5.2.3 Reducing the algal wet biomass of opportunistic species that generate important macroalgae deposits (e.g. Cladophora sp.) at levels below 2000 g/m² and hence the effects, especially in summer, by lowering the concentration of nutrients. Indicator 5.2.4 The 75th percentile of the Bac:Din (Bacillariophyceae: Dinophyceae) spring biomass ratio is more than to the 10:1 based on monitoring routine Indicator 5.3.1 Maintaining the spatial distribution of key perennial species (Cystoseira, Zostera) in stable limits (more than 60%) without fields fragmentation, due to anthropogenic activities.5.2.2. High water transparency can determine a vertical extension of the algae and phanerogams distribution. Indicator 5.3.2 The 95th percentile of bottom (up to 50 m due to the anoxic natural features of Black Sea) oxygen saturation values should be more than the threshold values as set out in the revised GES report All reported targets, related to causes (nutrients), direct effects (chlorophyll, transparency, etc), indirect effects (dissolved oxygen), are quite well considered by the programme. Generally, the data/information provided by the programme is sufficient for assessing progress towards achievement of the relevant environmental targets (difference between data provided and targets). Also, the program provides data/information and knowledge for regular updating of established targets, but it still needs to be improved (see Section 6). State relevant targets from other obligations (see section 2.1) that are addressed by the monitoring - maintenance of biodiversity; it can be negatively impacted by eutrophication; - prevent the deterioration of the status of all WB (no deterioration of the status of all WB) - protect, enhance and restore all SWB with the aim of achieving : the good ecological status and the good chemical status for natural WB by 2015 the good ecological potential and the good SW chemical status for artificial and heavy modified WB by 2015 – reducing pollution caused or induced by nitrates from agricultural sources; prevention of pollution by nitrates. – discharges from UWWTP to coastal sensitive areas which are subject to eutrophication (poor water exchange, large quantities of nutrients received) shall meet the requirements set up in Table 2, Annex 1 of Directive SAP (2009) 3.2 Long-term Ecosystem Quality Objectives (EcoQOs) EcoQO 3: Reduce eutrophication. EcoQO 4: Ensure Good Water Quality for Human Health, Recreational Use and Aquatic Biota. EcoQO 4a: Reduce pollutants originating from land based sources, including atmospheric emissions. To EcoQOs 3 and 4(a), BS SAP has awarded a number of management objectives, which overlap many of the MSFD provisions on evaluation, monitoring and determination of good environmental status. However, SAP indicators reflecting specific regional, cross-border issues and priorities, so they do not overlap perfectly over MSFD qualitative descriptors for determining GES. |
| 2.6 Spatial allocation | Table of where monitoring is required EEZ 12-nm zone Coastal waters Transitional waters MSFD X X X - Habitats - X X X WFD - - X X NiD - X X X UWWTD - - X X BWD - - X X BSC X X X X |
| 3 Monitoring concept |
| 3.1 General description of relevant subprogrammes in monitoring programme | 1. Seabed habitats - physical/chemical characteristics Elements/features monitored: Seabed habitats/Seabed habitats (physical/ chemical characteristics) Parameters: concentration of TOC; concentration of oxygen 2. Seabed habitats - community characteristics Elements/features monitored: Seabed habitats/Seabed habitats (biological characteristics), specific benthic species Parameters: Species composition 3. Benthic species - abundance and/or biomass Elements/features monitored: Seabed habitats/Seabed habitats (biological characteristics), specific benthic species Parameters: Species abundance (numbers of individuals or cover); Species biomass 4. Water column - physical characteristics Elements/features monitored: Water column/Oceanography - physical Parameters: transparency/turbidity of water column 5. Water column - physical characteristics Elements/features monitored: Water column/Oceanography - chemical Parameters: concentration of nutrients in water column; concentration of oxygen 6. Pelagic habitats - community characteristics Elements/features monitored: Water column/Oceanography - biological (phytoplankton, zooplankton) Parameters: Species composition; species abundance (number of individuals); species biomass 7. Plankton blooms (biomass, frequency) Elements/features monitored: Water column/Oceanography - biological (phytoplankton, zooplankton) Parameters: Concentration of Chlorophyll a 8. Nutrient inputs - land-based sources Elements/features monitored: Level of pressure at source/Nutrients Parameters: Input level of nutrient from land-based sources 9. Nutrient levels - in water column Elements/features monitored: Level of pressure in marine environment /Nutrients Parameters: concentration of nutrients in water column 10. Activities extracting living resources (fisheries including recreational, maerl, seaweed) Elements/features monitored: Activity/Fisheries incl. recreational fishing (fish and shellfish) Parameters: Distribution/extent in space and time, intensity 11. Activities extracting non-living resources (dredging) Elements/features monitored: Activity/Dredging Parameters: Distribution/extent in space and time, intensity 12. Activities producing food (aquaculture) Elements/features monitored: Activity/Aquaculture Parameters: Distribution/extent in space and time, intensity 13. Activities with permanent infrastructures (e.g. renewable energy, oil & gas, ports) or structural changes (e.g. coastal defences) Elements/features monitored: Activity/Energy production; Man-made structures (incl. construction phase) Parameters: Distribution/extent in space and time, intensity 14. Coastal human activities (e.g. tourism, recreational sports, ecotourism) Elements/features monitored: Activity/Recreation Parameters: Distribution/extent in space and time, intensity 15. Land-based activities Elements/features monitored: Activity/Coastal, riverine and atmospheric inputs from land - industrial discharges; Coastal, riverine and atmospheric inputs from land - agricultural run-off, forestry; Coastal, riverine and atmospheric inputs from land - municipal waste water discharge; Parameters: Distribution/extent in space and time, intensity 16. Effectiveness of measures Elements/features monitored: Existing measures Parameters: to be developed |
| 3.2 Description of monitoring network | NIMRD Monitoring network comprises 45 sampling stations (bottom depths within 5 – 60 m), covering the RO coastal and, partially, shelf waters (either waters strongly affected by the Danube’s inputs and coastal activities or marine waters, less affected by human induced eutrophication) (Fig. 1). Physical-chemical (transparency, DO, nutrients and TOC) and biological (chlorophyll, phytoplankton) parameters are monitored seasonally. Daily measurements (except for macroalgae) are carried out at two long-term on-coast stations (the first one dealing with the anthropogenic pressures in the Constanta area, the second one dealing with the Danube’s discharges – at Sulina) Fig. 1 Map of sampling stations of the environment routine monitoring carried out by NIMRD 12 sampling stations, in the coastal waters (Fig. 2), are selected for macroalgae monitoring (carried out in summer). Fig. 2 - Map of sampling stations of the macroalgae monitoring carried out by NIMRD RWNA - carries out monitoring activities mainly dealing with the land-based pressures. Sampling network comprises 35 stations covering transitional and coastal waters (Fig. 3). Nutrients and phytoplankton are monitored twice per year. Fig. 3 - Map of sampling stations of the environment routine monitoring carried out by RWNA – ABA GeoEcoMar Sampling network includes 45 stations, bottom depths within 15 – 200 m, covering the entire RO shelf (Fig. 4). Parameters monitored: Physical-chemical: - pressure/depth, dissolved oxygen/oxygen saturation, fluorescence (chlorophyll a), - in situ (CTD sensors – in water column); - Secchi depth, dissolved oxygen/oxygen saturation, nutrients (in water column, at depths according to water masses stratification, and at water-sediment interface) Biological: Chlorophyll a (in the water column) Frequency: 2 times/year Fig. 4 - Map of GeoEcoMar’s sampling network Black Sea Security System (BSSS – RO waters, Fig 5)) - 3 offshore moored observatories (bottom depths between 72 and 90 m) providing near-real time data (from surface layer and 20 m above seafloor) - 1 coastal station (bottom depth of 15m) Parameters monitored: DO, turbidity, Chlorophyll a BSSS is extending also in BG waters (2 offshore moored observatories) Fig. 5 - Map of offsore moored obsvervatories locations |
| 3.3 Threats, activities and measures | Which human activities will be measured by the programme Relevant activities themes/activities related to the programme are: Energy production/Marine hydrocarbon (oil and gas) extraction Extraction of living resources/Fisheries incl. recreational fishing (fish and shellfish) Extraction of non-living resources/ Dredging Food production/Aquaculture Man-made structures (incl. construction phase)/ Land/sea physical interaction: land claim, coastal defence; Port operations; Submarine cable and pipeline operations Recreation/Tourism and recreation incl. yachting Land-based activities/industries/Coastal and riverine and athmospheric inputs from land - industrial discharges; Coastal, riverine and atmospheric inputs from land - agricultural run-off, forestry and emissions; Coastal, riverine and atmospheric inputs from land – (municipal waste water discharge The programme will address to above mentioned activities by measuring either the distribution in space and time, intensity of some relevant activities. Also pressures resulted from these activities are subject to the current programme, either at source or in the marine environment. Which measures will be measured by the programme To be developed |
| 3.4 Data management | How and where are data managed? How and where can data be accessed? (General description – programme level) Data are reported (either as raw data or data products) through competent authority to EEA, BSC (through AGs – PMA, LBS, and CBD), etc. Data are also reported (either as metadata or raw data) in databases belonging to other projects (SeaDataNeet, SESAME, PERSEUS, MISIS, etc) from where can be accessed in accordance with the terms of such project |
| 4. Assessment |
| 4.1 Assessments | Existing assessments Provide information about or URL links to existing assessments (eg. Initial Assessment) MSFD (Art. 8) – Initial Assessment http://cdr.eionet.europa.eu/ro/eu/msfd8910/msfd4text/envuhwuaq Environmental Status Reports http://www.rmri.ro/Home/Products.EnvStatusReport.html State of Environment Report 2001-2006/7 http://www.blacksea-commission.org/_publ-SOE2009.asp |
| 4.2 Assessment of GES | Will assessment of GES be carried out by the programme Generally, the programme is able to provide adequate data and information enabling periodic assessment of environmental status (for coastal and, partially, shelf waters) and distance to and progress towards GES. The programme has to be considerably improved in terms of open waters (see Section 6). |
| 5. Literature |
|  | List of relevant literature Zampoukas, N., Piha, H., 2011, Review of Methodological Standards Related to the Marine Strategy Framework Directive Criteria on Good Environmental Status, Publications Office of the European Union, 53 pp. http://publications.jrc.ec.europa.eu/repository/handle/111111111/16069 Zampoukas, N., Piha, H., Bigagli, E., Hoepffner,N., Hanke, G., Cardoso, A., 2012, Monitoring for the Marine Strategy Framework Directive: Requirements and Options, Publications Office of the European Union, 42 pp., http://publications.jrc.ec.europa.eu/repository/handle/111111111/23169 Zampoukas, N., Piha, H., Bigagli, E., Hoepffner,N., Hanke, G., Cardoso, A., 2013, Marine monitoring in the European Union: how to fulfil the requirements for the MSFD in an efficient and integrated way, Marine Policy, 39, 349-351 http://publications.jrc.ec.europa.eu/repository/handle/111111111/27825 Marine Strategy Framework Directive – Task Group 5 Report Eutrophication. http://ec.europa.eu/environment/marine/pdf/5-Task-Group-5.pdf |
| 6. Activities required to implement the concept |
| 6.1 Changes to the current monitoring programme | Necessary changes and recommendations Describe necessary changes for the programme to cover the requirements of MSFD. Description in general terms. Recommendations and actions needed: increasing financial assistance and securing sustainable financing at national levels; better integration the MSFD monitoring with the monitoring requirements of the other directives (WFD, Habitats, NiD, etc) and regional sea conventions (BSC) better use and coordination of the existing capacities of all organizations dealing with monitoring programme (including monitoring infrastructure sharing); avoid overlapping of activities and efforts permanent agreements with other authorities/organisations in supporting the national monitoring programme (e.g. ROSA, RNA, Port Authorities, Offshore companies, etc) to strengthen the regional cooperation/harmonization between the Black Sea MS (to share their knowledge, identify best practises and ensure a harmonised monitoring methodology; adjust/increased temporal and spatial coverage; new monitoring tools to be developed (remote sensing tools, ferry boxes, smart buoys benthic observatories, ships-of-opportunity, models, etc.) monitoring of atmospheric deposition of nutrients need to be developed; coupled atmosphere-river-coastal sea models need to be developed at the regional scale; more research on development of an integrative tool to assess eutrophication (e.g BEAST); additional parameters to be included in order to develop existing/new indicators; more research on the primary production and algal biomass regulation; more research is needed for developing indicators/parameters that considered the effects of eutrophication on nutrients, DO, chlorophyll distribution within the water column (with special emphasis on the open waters); more research on natural background nutrient enrichment (e.g. import by upwelling; import from pristine/ good status rivers) for determination of pristine state and separation of naturally productive status from anthropogenically eutrophic status; climate change impacts on availability and transformation of nutrients and organic matter from land to the sea; Improving QA/QC Improving data management |
| 6.2 Gaps: GES information | If not yet adequate for data and information needs to assess GES, describe when the programme will be considered fully adequate in time for updating of monitoring programme in 2018 |
| 6.3 Plans: Plans for GES information | If the programme is not considered fully adequate for data and information needs to assess targets, describe what plans are in place to make it fully adequate (eg. to fill gaps in data methods or capacity). Describe timeframe, priorities and obstacles. The programme needs to be improved in terms of data acquisition and methodology used to define GES in the open waters (strengthen the cooperation between organizations, extension of spatial coverage, new monitoring tools for providing continuous and real-time/near real time data, usage of data products like satellites images, models, etc.). More research is needed for developing an integrative tool (e.g. BEAST, TRIX) to provide a complete picture of eutrophic conditions, thus a better assessing of environmental status. Also the programme has to be improved for providing more data/information and knowledge, related to some quite poor approached indicators/parameters (e.g. benthic to pelagic shifts; toxic algal blooms; nutrient ratio; nutrient fluxes, nutrients input, including atmospheric input; vertical distribution of nutrients, chlorophyll, etc.), required for a better understanding and/or more robust GES definitions. |
| 6.4 Gaps: Target information | If not yet adequate for data and information needs to assess GES, describe when the programme will be considered fully adequate In time for the next assessment in 2018 |
| 6.5 Plans: Plans for information on targets | If the programme is not considered fully adequate for data and information needs to assess targets, describe what plans are in place to make it fully adequate (e.g. to fill gaps in data methods or capacity). Describe timeframe, priorities and obstacles. The programme needs to be improved in terms of data acquisition for defining/updating targets values in the open waters, new monitoring tools for providing continuous and real-time/near real time data, usage of data products like satellites images, models, etc). Also, some improvements have to be done in terms of coordination of monitoring effort (at national and sub-regional level), harmonization of sampling methodologies and analytical procedures (between organisations dealing with monitoring activities), QA/QC, etc. for providing more reliable data/information necessary for regularly updating of targets. |
| 6.5 Plans: Plans for information on measures | If relevant: If the programme is not considered fully adequate for data and information needs to assess measures describe what plans are in place to make it fully adequate (eg. to fill gaps in data methods or capacity). Describe timeframe, priorities and obstacles. To be developed |